## Slide 1: A Corporate Accounting and Reporting Standard
Training Curriculum
Notes: A Corporate Accounting and Reporting Standard

## Slide 2: Lesson Modules
Notes: OK, there are three main accounting steps in designing an invcentory. We~ve already covered 2 of these – setting operational and organizational boudnaries.
The third step and the focus of this presentation is setting base years and using those base years to track progress over time .

## Slide 3: Tracking Emissions Over Time
Lesson 5

## Slide 4: Learning Objectives
In this lesson, you will learn:
How to assess your company’s emissions trends
How to choose a base year
Why you may need to re-calculate base year emissions
How to recalculate base year emissions

## Slide 5: Base year
Base year= the period in history against which an organization’s emissions are tracked over time
Advantages
Track progress towards reduction targets
Put effects of inventory changes into context
Year
2009
2010
Mt CO2e/ yr
2008
2007
35,000
42,000
40,000
33,000
Base Year
2010: Increase of ~21% over base period emissions
Notes: So, what is a base year? The base year is the year in history against which an organization’s emissions are tracked over time. The Corp Std requires companies to set base years as they are so important for inventory design for several reasons:
They help companies track progress towards reduction targets
They help put the effects of changes in inventory practices into context.
And we’ll cover both these applications later in this lesson.

## Slide 6: Choosing a Base Year
Select the earliest year with verifiable emissions data for required Scopes
Specify why you chose that particular year
If emissions fluctuate dramatically annually, consider averaging emissions over a series of consecutive years as your base year
2005
2006
2007
2008
Scope 1 | 
Scope 2 | 8,000
Scope 3 | 
Scope 1 | 
Scope 2 | 8,500
Scope 3 | 
Scope 1 | 4,500
Scope 2 | 9,000
Scope 3 | 
Scope 1 | 4,500
Scope 2 | 9,500
Scope 3 | 11,000
Notes: We would recommend that a company select as the base year the earliest year for which verifiable data are available for the required scope – that is for scopes 1 and 2.
So, in this example, the company has only scope 2 data for 2005 and 2006 and so would not select either of these years as the base yr. Scope 1 and 2 data are instead available for 2007 and so this year could be the base yr.
In addition to requiring that companies set base years, the Corp Std also requires companies to explain why that particular yr was chosen.
Also, a fundamental consideration in selecting a base year is that it be representative of a companys emissions profile. Otherwise, if the chosen base year were not representative, then it will not allow for meaningful comparisons of performance over time and would basically be useless. So, if emissions do flcutuate dramatically over time, the Corp Std also recommends that companies consider averaging emissions over a series of consecutive years to derive an average base year profile. And the important pt here is that the yrs should be consecutive – an averaged base yr shouldn’t be based on a set of non-consecutive years.

## Slide 7: Recalculating Base Year Emissions
Retroactively recalculate base year emissions to reflect company changes that could compromise consistency and relevance of emissions data
Develop a base year emissions recalculation policy and apply it in a consistent manner
State the basis and context for any recalculations
Notes: Once a base year has been selected and an inventory has been developed for that base year, it is important to understand when that inventory needs to be recalculated to ensure consistent inventory data and boundaries over time and to ensure that base periods remain useful as a basis for tracking performance.
The Corp Std requires companies to do a number of things in this regard:
- Retroactively recalculate base year emissions to reflect company changes that could compromise consistency and relevance of emissions data…over time.
- Develop a base year emissions recalculation policy and apply it in a consistent manner… over time. This policy would essentially state when changes are significant enough to trigger recalculations, and more about that in a second. .
- Companies would need to report in their inventories when and why they have recalculated their base period data.

## Slide 8: Recalculate for
Significant changes in structure of organization
Significant changes in calculation methodology
  Improved emission factors
  Improved activity data
Discovery of significant errors or smaller errors that are collectively significant
Notes: So, what factors would cause recalculation? Well, in the Corp Standard the main reasons base years have to recalculated are when:
…
…
…
Conceptually, changes in org structures can be more difficult to understand that changes in calculation methods or the discovery of errors, so what I want to do is spend a few slides explaining how org changes affect base year inventories. But I’ll do that after first explaining what the term significance means – as you can see, significance is a common term that is fundamental to all 3 of these requirements, so what does it mean exactly?

## Slide 9: Significance Threshold
Significance threshold: a criterion used to determine whether a change is significant enough to warrant recalculation
The GHG Protocol does not specify a significance threshold
Each organization must define what significance threshold will trigger base year recalculations
Notes: To determine whether a change is significant it is evaluated against a significance threshold. So, for instance, a threshold level of sig might be 5%, such that if a change in inventory boundaries or methodology results in a change in the base year inventory that is equal to or more than 5% of the total emissions reported in that inventory, then that change is considered signfiicant.
The Copr Std doesn’t actually require or recommend a specific sig threshold. However, many GHG programs would do so - (e.g., Brazil program: 5%).
Instead, what we find, is that the Corp Std simply requires each company to define its own threshold and apply that threshold consistently across time.

## Slide 10: Structural Changes
Structural change: transfer of ownership or control of emitting activities from one company to another
  Mergers, acquisitions, and divestments
  Outsourcing or in-sourcing of emitting activities
    Don’t recalculate if out- or in-sourced activities were previously included in a different Scope
Recalculate base year emissions for structural changes
Notes: So, let’s get back to the issue of recalculating base year inventories for changes in org structures. Here, structural change is defined as………
And different type's of structural changes exist. One is the purchase/divestment of operations that existed in base year. Another is outsourcing or in-sourcing of emitting activities. And we’ll have some examples of these changes in a minute. Both these types of structural changes will trigger base yr recalculations, assuming the change meets the significance threshold. The one exception to be mindful of is out-sourcing or in-sourcing – if the out-sourced or in-sourced activities were previously included in a different scope within an inventory, there is no need to recalculate the inventory. So, for example, if an activity was previously reported in scope 3, but was subsequently in-sourced and moved to scopes 1 or 2, there would be no need to recalculate the base yr inventory because the emissions were already reported by the company.
Another general point is that while a single structural change might not have a sig impact on the base period, the cumulative impact of multiple changes might be significant. So, when assessing the need to recalculate base yr inventories, it is really necessary to consider the cumulative impact of multiple changes.

## Slide 11: Recalculating for Structural Changes
(assuming B existed in A’s base year)
A should include B’s emissions in
  A’s base year inventory and
  A’s current year inventory
(assuming B existed in A’s base year)
A should exclude B’s emissions from
  A’s base year inventory and
  A’s current year inventory
If A acquires B
If A divests of B
Notes: OK, so Here is a basic example of recalculating base yr inventories for structural changes.
In the first general case, if Company A acquires B, Company A would include the emissions of Company B in both its current inventory and base yr inventory. This is assuming that company B, of, course, existed in Company A’s base year.
Conversely, If Company A divests Company B, then it should exclude the emissions of Company B from both its current inventory and base yr inventory. Again, this is assuming that Company B existed during Company A’s base year.

## Slide 12: Changes NOT Requiring Recalculation
Changes involving facilities that did not exist in the base year
Out-sourcing/in-sourcing of activities previously reported under a different Scope
Organic growth or decline
Notes: Just to make clear, I thought it would be useful to list on a single slide the various instances when org changes never trigger recalculations of the base yr inventory.
We’ve gone through two of these already – we’ve already seen that recalculations are not necessary when (1) and (2).,,,,,,,,
But you should also note that recalculations are not necessary when a company has only experienced organic growth or decline, rather than a structural change. And by organic growth I mean increases or decreases in production output or closures/opening of operating units that are owned by the reporting company. So, for example, if a company simply grows by adding on more manufacturing capacity, perhaps by building a new plant, that growth does not constitute a structural change and should never trigger recalculations of the base year inventory.

## Slide 13: Recalculation: Acquisition
3
Company acquires unit C
1
Base Year
2
Increase in production
emissions
Facility C emissions
1
emissions
2
3
Recalculated Figures
Recalculating 2nd year: optional
25
25
15
20
20
20
30
30
25
30
30
20
30
30
25
30
30
Notes: So, let’s just have a couple of graphical examples to illustrate how base year calculations work in practice. It’s often easier to visualize recalculations this way.
This example shows how recalculations would work if a company acquired a new operating unit.
Company emits 50 tons in its base year
Experiences an increase in production in yr 2 and emits 60 tons (this does not trigger base year recalculation)
Again emits 60 tons in yr 3 but also acquired a unit at the beginning of the year that emitted an additional 20 tons
When developing its inventory for the current (third) year, the company just adds on the 20 tons of emissions from the acquired unit to its 60 emissions.
But for its base yr inventory, because the emissions from the acquired unit are considered significant, the company has to recalculate its base yr emissions and it does this by adding the 15 tons of emissions the unit emitted in year 1 to its base year.
It could also recalculate the inventory for the second year, but that is optional.

## Slide 14: Recalculation: Divestment
1
Base Year
emissions
1
2
3
emissions
3
Company divests unit C
Recalculated Figures
Recalculating 2nd year: optional
2
Increase in production
30
30
30
30
30
30
25
25
25
30
30
30
25
25
25
30
30
Notes: Conversely, This slide just shows how recalculations would work if a company divested itself of an operating unit.
Here the company is initially comprised of 3 units. Unit C at the top emits 25 tons in the base yr and 30 tons in yr 2. In yr 3 the company divests unit c, so it would remove the unit C’s emissions from its base year and (optionally) the intervening inventory for year 2.

## Slide 15: Recalculation: Acquisition of facility not existing in base year
1
Base Year
emissions
Facility C emissions
1
emissions
2
3
3
Company acquires unit C
did NOT exist
Do not recalculate base year
Recalculate 2nd year:
Optional
Recalculated Figures
15
2
Increase in production
30
30
20
25
30
25
30
20
25
30
30
25
30
30
20
Notes: And, finally, here a company has acquired a facility that did not exist in its base year. So, the unit emitted nothing in year 1. The unit did exist in yr 2, however, and it emitted 15 tons in yr 2, and 20 tons in yr 3. In this case, the company does not recalculate its base yr inventory, although it could recalculate its inventory for yr 2 if it wanted to.

## Slide 16: Timing of Recalculation
If structural changes occur in the middle of the year, recalculate for the entire year
This “all-year” option
  is less complicated
  gives the same result as calculating for the remainder of the year and making adjustments
  avoids recalculations for subsequent years
Notes: Before we go any further, I just wanted to spend a slide on best practices for recalculating emissions based on when within the reporting cycle the org change actually occurs.
And, In general, if structural changes occur in the middle of the reporting cycle, then best practice is to reclaulate for the entire year. And this “all year” option is generally recommended because it gives the same result as calculating for the remainder of the year and making adjustments, and it is also less complicated, because it will avoid having to make recalculations for subsequent years.
[…. Otherwise, in futuire yras, a company would be comparing the full yr performance of the uniot to a base yr, where the unit was only effectively operational for half the year]

## Slide 17: Example 1
It opens a new factory in year 2 to meet this demand.
Should the base year emissions be recalculated?
The demand for Company A’s products increases.
No
(don’t recalculate for organic growth)
Base year | Year 2 | Year 3
50,000 | 80,000 | 83,000
Notes: OK. Lets have some more examples to illustrate when recalculations are and are not needed.

## Slide 18: Example 2
Should the base year emissions be recalculated?
The demand for Company D’s products increases.
It acquires an older factory from Company E in year 2 to meet this demand.
Yes
(recalculate for acquisitions)
Base year | Year 2 | Year 3
50,000 | 80,000 | 83,000

## Slide 19: Example 3
Should the base year emissions be recalculated?
Original emissions calculations:
Later, an error was detected.
Emissions were then correctly calculated:
Company sets a 5% significance threshold for errors
Yes
(errors met 5% significance threshold, triggering recalculation)
Base year | Year 2 | Year 3
90,000 | 80,000 | 85,000
Base year | Year 2 | Year 3
325,000 | 300,000 | 330,000

## Slide 20: Review
Situation | Base year recalculation?
Company acquires another company | Yes if acquired company existed in base year of reporting company
Production of steam is out-sourced | No emissions move from Scope 1 to Scope 2
Company produces more and emissions increase | No
Company installs continuous emissions monitoring systems and collects more accurate data | Yes if more accurate data show changes that meet significance threshold
Notes: So, let’s review some other situations quickly and see if they result in recalculations.
…..
Situation 2: Here recalculations are not needed because the emissions from outsources steam production are scope 2 and so will have to still be reported within the inventory.
…..

## Slide 21: Summary
Base year: the year in history against which an organization’s emissions are tracked over time
Define your organization’s recalculation policy
  Define significance threshold to trigger base year recalculation
Recalculate for
  structural changes
  changes in calculation methodology
  discovery of significant errors
Don’t recalculate for
  organic growth or decline
  Changes involving facilities that didn’t exist in base year
  Out-/in-sourcing of activities previously accounted for in different Scope
Notes: So, in summary, the base year is the year …..
Companies need to define a recalculation policy, which essentially means they need to define a sig threshold to determine when recalculations are needed

## Slide 22: Further Reading
  The Greenhouse Gas Protocol: A Corporate Accounting & Reporting Standard
  Chapter 5: Tracking Emissions Over Time
  Chapter 11, Step 4: Choose the Target Base Year
  Appendix E: Base Year Recalculation Methodologies for
  Structural Changes (http://www.ghgprotocol.org/standards/corporate-standard)
  Hot Climate, Cool Commerce: A Service Sector Guide to Greenhouse Gas Management
  Part 3, Step 5: Establishing an Emission Reduction Target
  ISO 14064-1
  Section 5.3 Base-year GHG inventory